## Slide 1: Accelerating Network Intensive Workloads Using the DPDK netdev
November 2014
OVS Fall Conference 2014
Intel

## Slide 2: Legal Disclaimers
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL PRODUCTS. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. EXCEPT AS PROVIDED IN INTEL'S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO SALE AND/OR USE OF INTEL PRODUCTS INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
A "Mission Critical Application" is any application in which failure of the Intel Product could result, directly or indirectly, in personal injury or death. SHOULD YOU PURCHASE OR USE INTEL'S PRODUCTS FOR ANY SUCH MISSION CRITICAL APPLICATION, YOU SHALL INDEMNIFY AND HOLD INTEL AND ITS SUBSIDIARIES, SUBCONTRACTORS AND AFFILIATES, AND THE DIRECTORS, OFFICERS, AND EMPLOYEES OF EACH, HARMLESS AGAINST ALL CLAIMS COSTS, DAMAGES, AND EXPENSES AND REASONABLE ATTORNEYS' FEES ARISING OUT OF, DIRECTLY OR INDIRECTLY, ANY CLAIM OF PRODUCT LIABILITY, PERSONAL INJURY, OR DEATH ARISING IN ANY WAY OUT OF SUCH MISSION CRITICAL APPLICATION, WHETHER OR NOT INTEL OR ITS SUBCONTRACTOR WAS NEGLIGENT IN THE DESIGN, MANUFACTURE, OR WARNING OF THE INTEL PRODUCT OR ANY OF ITS PARTS.
Intel may make changes to specifications and product descriptions at any time, without notice. Designers must not rely on the absence or characteristics of any features or instructions marked "reserved" or "undefined". Intel reserves these for future definition and shall have no responsibility whatsoever for conflicts or incompatibilities arising from future changes to them. The information here is subject to change without notice. Do not finalize a design with this information.
The products described in this document may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Contact your local Intel sales office or your distributor to obtain the latest specifications and before placing your product order.
Copies of documents which have an order number and are referenced in this document, or other Intel literature, may be obtained by calling 1-800-548-4725, or go to: http://www.intel.com/design/literature.htm
Intel processor numbers are not a measure of performance. Processor numbers differentiate features within each processor family, not across different processor families: Go to: Learn About Intel® Processor Numbers
Intel, the Intel logo, Intel Atom, and Xeon are trademarks of Intel Corporation in the U.S. and/or other countries.
*Other names and brands may be claimed as the property of others.
Copyright © 2013 Intel Corporation. All rights reserved

## Slide 3: Agenda
Motivation
Architecture
Results
Futures

## Slide 4: Motivation
Chart: Open vSwitch with DPDK Phy-Phy Latency
| 64 | 512 | 1024 | 1448 | 1500
Max Latency Kernel | 3261 | 912 | 961 | 1032 | 1040
Avg Latency Kernel | 1802 | 627 | 79 | 121 | 63
Min Latency Kernel | 342 | 193 | 17 | 53 | 37
Chart: Open vSwitch Phy-Phy Throughput
| 64 | 512 | 1024 | 1448 | 1500
PPS Line Rate | 14880952.381 | 2349624.0602 | 1197318.0077 | 851498.6376 | 822368.4211
PPS OVS Kernel | 1379000 | 1174843 | 1197296 | 851485 | 822353
Low packet rate insufficient for packet-processing intensive workloads (e.g. NFV)
Latency & jitter sensitive workloads impacted

## Slide 5: Performance Data
  Intel(R) Xeon(R) CPU E5-2680 v2 processor, 2.80GHz , 25M Cache
  Intel(R) C602 Chipset
  DDR3 1600MHz, 8 x dual rank registered ECC 8GB (total 64GB), 4 memory channels per socket Configuration, 1 DIMM per channel
  Operating System: Fedora 20
  Kernel version: 3.15.6-200.fc20.x86_64
  Open vSwitch: 2.3.0-1.fc20.x86_64
  Accelerated Open vSwitch with DPDK-netdev commit id:0d2cb7087c8d058466bb1f6af2426a27fdd388c3
  Intel(R) DPDK 1.7.0
  IxExplorer 6.60.1000.11 GA
Ixia 10G Tester
Server
Socket 1 (10 cores)
OVS with DPDK
Phy – Phy (Tx Received Pkts)
Socket 2 (10 cores)
(unused)
BIOS Settings | Setting
Enhanced Intel SpeedStep® | DISABLED
Processor C3 | DISABLED
Processor C6 | DISABLED
Intel® Hyper-Threading Technology (HTT) | DISABLED
Intel® Virtualization Technology | ENABLED
Intel® Virtualization Technology for Directed I/O (VT-d) | DISABLED
MLC Streamer | ENABLED
MLC Spatial Prefetcher | ENABLED
DCU Data Prefetcher | ENABLED
DCU Instruction Prefetcher | ENABLED
Direct Cache Access (DCA) | ENABLED
CPU Power and Performance Policy | Performance
Memory Power Optimization | Performance Optimized
Intel® Turbo boost | OFF
Memory RAS and Performance Configuration -> NUMA Optimized | ENABLED
Results will vary depending on software, workloads and system configuration

## Slide 6
Available at openvswitch.org (https://github.com/openvswitch/ovs )
Version of Open vSwitch integrating DPDK available as of 3/19/14
To be released in ver 2.4 of openvswitch
Minimal architectural changes through use of additional “netdev” interface
Used in conjunction with User Space Open vSwitch module (Kernel switch not used)
User space switch reworked by VMware to optimize for performance
Permissive license in User Space Switch
Currently Supports in Mainline Git or Patches :
  Full match / action set
  DPDK Physical Ports
  VM – VM , VM – Physical Port
    DPDK ivShmem Ports
    DPDK vHost Ports
  L3 tunneling (VXLAN) support
  Metering
Linux User Space
OVS Daemon
ofproto
netdev
ofproto-dpif
dpif provider
netdev provider
Linux Kernel Space
Physical I/O
Physical I/O
Data Plane Switch
User Space Switch
DPDK Framework
Rx
Tx
Rx
Tx

## Slide 7: Open vSwitch® with DPDK Architectural Approach
ovs-switchd
NIC
DPDK
Libraries
PMD
DPDK
netdev
ovs kernel module
qemu
VM
virtio
kernel packet processing
User Space Forwarding
socket
TAP
netdev
User Space
External
SDN Controller
ovsdb
OF
ovsdb server
ovs-switchd
qemu
VM
virtio
IVSHEM
vHost
qemu
VM
shmem
DPDK
Tunnels
Kernel Space

## Slide 8: Results
Near 10G line rate
50x lower latency for small packets
Chart: Open vSwitch with DPDK Phy-Phy Latency
| 64 | 512 | 1024 | 1448 | 1500
Max Latency uS | 430 | 193 | 192 | 190 | 193
Average Latency uS | 36 | 106 | 105 | 101 | 104
Min Latency uS | 8 | 11 | 13 | 9 | 9
Max Latency Kernel | 3261 | 912 | 961 | 1032 | 1040
Avg Latency Kernel | 1802 | 627 | 79 | 121 | 63
Min Latency Kernel | 342 | 193 | 17 | 53 | 37
Chart: Open vSwitch Phy-Phy Throughput
| 64 | 512 | 1024 | 1448 | 1500
PPS Line Rate | 14880952.381 | 2349624.0602 | 1197318.0077 | 851498.6376 | 822368.4211
PPS OVS Kernel | 1379000 | 1174843 | 1197296 | 851485 | 822353
PPS OVS DPDK | 13187355 | 2349555 | 1197296 | 851484 | 822354

## Slide 9: Futures
DPDK netdev bypasses the kernel, meaning some loss of functionality
Would both userspace and kernel space paths be useful?
  The Bifurcated Driver for DPDK uses hardware classification to put frames either through the kernel path, through the DPDK netdev, or into a virtual function
What are the major gaps in the userspace pipeline?
  Userspace Packet Filtering would allow functions such as security, ACLs, NAT or deep packet inspection to happen after a frame is pulled into userspace over the DPDK netdev
  A Userspace Connection Tracker would enable applications needing stateful flow tracking
  These enhancements don’t necessarily need to be part of OVS, just accessible and efficient in userspace for OVS to use
Desire to see userspace OVS become a first class data plane

## Slide 10: Bifurcated Driver
ip (route)
User
driver
net-filter
OVS-kernel
DPDK netdev
OVS
nft
ethtool
kernel
management interface
data path
Hardware
Classification
Flow-based classification to be accelerated by hardware.
Finer Granularity control versus SR-IOV
Kernel-bypass/
zero-copy
ip
Application

## Slide 11: Desirable Augmentation to Data Plane
ovs-switchd
NIC
DPDK
Libraries
PMD
DPDK
netdev
ovs kernel module
qemu
VM
virtio
kernel packet processing
User Space Forwarding
socket
TAP
netdev
User Space
External
SDN Controller
ovsdb
OF
ovsdb server
ovs-switchd
qemu
VM
virtio
IVSHEM
vHost
qemu
VM
shmem
DPDK
Tunnels
Kernel Space
Packet Filter
Conn Tracker
Must handle high packet rates

## Slide 12: Summary
The DPDK netdev greatly increases packet receive
Bypasses kernel, meaning some loss in functionality
Time to consider putting high performance packet processing in userspace
Can use the bifurcated driver to have a fast lane and a ‘every kernel filter applied’ lane
Long term approach is to move more functionality into userspace
Feedback on architecture, code and additional benchmark tests is appreciated

## Slide 13: Performance Data
  Intel(R) Xeon(R) CPU E5-2680 v2 processor, 2.80GHz , 25M Cache
  Intel(R) C602 Chipset
  DDR3 1600MHz, 8 x dual rank registered ECC 8GB (total 64GB), 4 memory channels per socket Configuration, 1 DIMM per channel
  Operating System: Fedora 20
  Kernel version: 3.15.6-200.fc20.x86_64
  Open vSwitch: 2.3.0-1.fc20.x86_64
  Accelerated Open vSwitch with DPDK-netdev commit id:0d2cb7087c8d058466bb1f6af2426a27fdd388c3
  Intel(R) DPDK 1.7.0
  IxExplorer 6.60.1000.11 GA
Ixia 10G Tester
Server
Socket 1 (10 cores)
OVS with DPDK
Phy – Phy (Tx Received Pkts)
Socket 2 (10 cores)
(unused)
BIOS Settings | Setting
Enhanced Intel SpeedStep® | DISABLED
Processor C3 | DISABLED
Processor C6 | DISABLED
Intel® Hyper-Threading Technology (HTT) | DISABLED
Intel® Virtualization Technology | ENABLED
Intel® Virtualization Technology for Directed I/O (VT-d) | DISABLED
MLC Streamer | ENABLED
MLC Spatial Prefetcher | ENABLED
DCU Data Prefetcher | ENABLED
DCU Instruction Prefetcher | ENABLED
Direct Cache Access (DCA) | ENABLED
CPU Power and Performance Policy | Performance
Memory Power Optimization | Performance Optimized
Intel® Turbo boost | OFF
Memory RAS and Performance Configuration -> NUMA Optimized | ENABLED
Results will vary depending on software, workloads and system configuration