## Slide 1: OVS and L7 classification (DPI) Demo part 1: L7 Firewall, L7 QoS Demo part 2: L7 Service Chaining
Open vSwitch conference, November 2015
Franck Baudin

## Slide 2: Agenda
OVS & L7 Classification insights
Demo part 1: L7 Firewall and L7 QoS
Demo part 2: L7 Service Chaining
Next steps
Annexes: demos screenshots, collaterals

## Slide 3: Asynchronous L7 classification: general overview
 Delay L7 classification
  1st packet already out
 Minimum jitter
  datapath best/worst case
 Garanted latency
  datapath worst case
 No HEAD of line blocking
  by async. design
RX & dispatch
datapath
DPI engine
TX
Flow table
L7, application ID
100%
10%
steer, QoS, drop…
copy
async.
update

## Slide 4: Asynchronous L7 classification with OVS via the conntrack table
RX & dispatch
OVS kernel
datapath
L7 classifier
(DPI engine)
TX
100%
NL_CT
conntrack
table
mark
label
10%
QoS, drop, output …
Linux Kernel
Linux user space
LOCAL OVS port
(L7PORT)
Flow Table
skbuff->CT->mark

## Slide 5: L7 rule-set hierarchy
attach CT
resubmit table 1
Table 0
resubmit table 2
Table 1
CLASSIFIED
resubmit table 2
output L7PORT
NORMAL
Table 2
DROP
NORMAL
SSH
SSH
TCP port 22
L7 matcher
L1-4 matcher
action

## Slide 6: Agenda
OVS & L7 Classification insights
Demo part 1: L7 Firewall and L7 QoS
Demo part 2: L7 Service Chaining
Next steps
Annexes: demos screenshots, collaterals

## Slide 7: Demo overview
http server (vmlinuz) => FULL SPEED
bittorrent (vmlinuz) => RATE LIMIT
ssh on port 22 => PASS
ssh on port 5022 => DROP
server
OVS** + L7 classifier
client
** https://github.com/justinpettit/ovs.git, 4a5c0cf
L7
L7

## Slide 8: Agenda
OVS & L7 Classification insights
Demo part 1: L7 Firewall and L7 QoS
Demo part 2: L7 Service Chaining
Next steps
Annexes: demos screenshots, collaterals

## Slide 9: Dynamic Service Function Chaining: concept overview
L7 Service Classifier
access
FW
LB
PC
RL
SFF
Service Function Forwarder
Internet
WEB
BITTORRENT

## Slide 10: Demo topology
br-internet
br-access
br-sff
br-classifier
L7 classifier
(DPI engine)

## Slide 11: br-classifier OVS rules
# port1: access, port2: internet, port3: SFF
table=0, priority=3,in_port=3 actions=resubmit(,30) # From SFF
table=0, priority=2,ct_state=-trk,ip actions=ct(table=1) # IP traffic: attach CT
table=0, priority=1,in_port=1 actions=output:2 # non IP traffic, bypass
table=0, priority=1,in_port=2 actions=output:1 # non IP traffic, bypass
# Send packet to L7 classifier when required (classif in progress, signaling protocol like SIP or FTP)
table=1, priority=2,ct_state=+new actions=ct(commit),output:4,resubmit(,2)
table=1, priority=1,ct_mark=0x80000000/0x80000000 actions=resubmit(,2) # classif done, offloaded
table=1, actions=output:4,resubmit(,2) # under classif
# Send ssh (0xc6) in Encrypted chain (tos=92), bittorrent (0xf) in Peer2Peer (tos=96)
table=2, priority=11,ct_mark=0xc6/0xffff,in_port=2 actions=mod_nw_tos:92,output:3 # to SFF
table=2, priority=10,ct_mark=0xf/0xffff,in_port=2 actions=mod_nw_tos:96,output:3 # to SFF
table=2, priority=0,in_port=1 actions=output:2 # default policy
table=2, priority=0,in_port=2 actions=output:1 # default policy
# Chains exit, remove the SFC mark (really matters when using NSH, MPLS, VLANs… instead of TOS)
table=30, priority=10,ip,in_port=3,nw_tos=96 actions=mod_nw_tos:0,output:1
table=30, priority=11,ip,in_port=3,nw_tos=92 actions=mod_nw_tos:0,output:1
CHAIN NAME | RSP | TOS | CHAIN
Encrypted | Encrypted-Path-23 | 92 | firewall -> qos
Peer2Peer | Peer2Peer-Path-24 | 96 | qos

## Slide 12: Br-SFF rules
table=0, priority=2,dl_vlan_pcp=1 actions=resubmit(,30)
table=0, priority=1,ip actions=move:NXM_OF_IN_PORT[0..11]->NXM_OF_VLAN_TCI[0..11],mod_vlan_pcp:1,resubmit(,10)
table=10, priority=1000,ip,dl_vlan=9,dl_vlan_pcp=1 actions=move:NXM_OF_IP_TOS[]->NXM_NX_REG0[0..7],load:0xff->NXM_NX_REG1[0..7],resubmit(,20)
table=10, priority=255,ip,dl_vlan=21,dl_vlan_pcp=1,nw_tos=92 actions=load:0x5c->NXM_NX_REG0[0..7],load:0xfe->NXM_NX_REG1[0..7],resubmit(,20)
table=10, priority=254,ip,dl_vlan=23,dl_vlan_pcp=1,nw_tos=92 actions=load:0x5c->NXM_NX_REG0[0..7],load:0xfd->NXM_NX_REG1[0..7],resubmit(,20)
table=10, priority=255,ip,dl_vlan=23,dl_vlan_pcp=1,nw_tos=96 actions=load:0x60->NXM_NX_REG0[0..7],load:0xfe->NXM_NX_REG1[0..7],resubmit(,20)
table=20, priority=255,reg0=0x5c,reg1=0xff actions=mod_vlan_vid:20,mod_vlan_pcp:1,resubmit(,30)
table=20, priority=254,reg0=0x5c,reg1=0xfe actions=mod_vlan_vid:22,mod_vlan_pcp:1,resubmit(,30)
table=20, priority=255,reg0=0x60,reg1=0xff actions=mod_vlan_vid:22,mod_vlan_pcp:1,resubmit(,30)
table=20, priority=0 actions=mod_vlan_vid:9,mod_vlan_pcp:1,resubmit(,30)
table=30, priority=1000,ip,dl_vlan_pcp=1 actions=move:NXM_OF_VLAN_TCI[0..11]->NXM_NX_REG2[0..11],strip_vlan,output:NXM_NX_REG2[0..11]
table=30, priority=1,ip actions=drop
CHAIN NAME | RSP | TOS | CHAIN
Encrypted | Encrypted-Path-23 | 0x5c | firewall -> qos
Peer2Peer | Peer2Peer-Path-24 | 0x60 | qos
For reference only, too complex for a quick live explanation
Key points
  Map NSH NSP/NSI into REG0/REG1 (will ease implementation with NSH)
  Multiple SFF support (VNFs distributed among multiples compute nodes)

## Slide 13: Agenda
OVS & L7 Classification insights
Demo part 1: L7 Firewall and L7 QoS
Demo part 2: L7 Service Chaining
Next steps
Annexes: demos screenshots, collaterals

## Slide 14: Next steps
L7 aware management: OpenStack, OVN, ODL, GBP, FWaaS,…
Optimization: zero copy instead of a copy over a port/tap
  Requires a new kernel module, kind of inverted PF_RING
  Qosmos developed one, to be open sourced when needed
Porting within DPDK datapath
  L7 classifier running as a DPDK secondary process
  Interconnected via a DPDK ring
L7 visibility: enriched IPFIX with L7 classification
  Exporting ct_mark and ct_label
  Exporting associated metadatas (MIME type, SQL request, filename, …)
    Need to add a scratchpad in conntrack, with NL_CT accessors…
L7 aware Service Chaining: extend OVS NSH actions (which are under dev.)
  NSH type 1 with L7 application ID (aka ct_mark/ct_label)
  Metadata extraction and NSH type2

## Slide 15
Thanks! Questions?

## Slide 16: Annexes
L7 classification insights
Demo part 1: configuration details & step by step screenshots
Demo part 2: screenshots

## Slide 17: L7 classification insights: functional
L7 classification is based on network conversations analysis
  Conversation: (client -> server) and (server -> client)
    2 OpenFlow flows
  Direct mapping on Linux: conntrack
L7 classification is based on payload
  IP reassembly
  TCP segment reordering
Most applications are classified with the first packet of payload
  … so right after TCP handshake
  some applications requires more packets (skype, bittorrent, …)
  Signalization protocols generating RELATED conversations to be analyzed even if classified (ex: ftp & ftpdata)
  If the application is not recognized after N packets: classified as “unknown”

## Slide 18: DPI engine performances on Intel(R) Xeon(R) E5-2690 v3 @ 2.60GHz
9Gbps/core
Scalable on a socket
  Best design: one instance per socket
Realistic traffic profile
  real application sessions
    HTTP, DNS, Bittorrent, SIP, POP3,…
  Average frame size: 799.53 bytes
  Breakingpoint traffic generator
    North American Wireless Carrier Weekday profile
Chart: Gbps vs core number (2 HT)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Gbps | 9.726 | 18.717 | 27.988 | 36.612 | 45.74 | 54.696 | 63.48 | 72.046 | 80.891 | 89.136 | 97.727 | 105.287
Notes:   ~100k sessions/second per 10 Gbps
  ~2Mpps per 10 Gbps

## Slide 19: Annexes
L7 classification insights
Demo part 1: configuration details & step by step screenshots
Demo part 2: screenshots

## Slide 20: Demo part 1, L7 Firewall, L7 QoS: ovs configuration
ovs-ofctl del-flows br0
# table 0: attach a conntrack to all ip packets
# ---------------------------------------------
ovs-ofctl add-flow br0 "priority=40000,table=0,ip,ct_state=-trk,actions=ct(table=1)"
ovs-ofctl add-flow br0 "action=NORMAL"
# table1: send a copy of the packets to the L7 classifier
# -------------------------------------------------------
ovs-ofctl add-flow br0 "table=1,priority=2,ct_state=+new,actions=ct(commit),output:$L7PORT,resubmit(,2)"
ovs-ofctl add-flow br0 "table=1,priority=1,ct_mark=0x80000000/0x80000000 actions=resubmit(,2)"
ovs-ofctl add-flow br0 "table=1,priority=0,actions=output:$L7PORT,resubmit(,2)"
# table2: packet behaviour, depending on ct_mark
# ----------------------------------------------
# offload == ct_mark/0x80000000
# L7 proto == ct_mark/0x7FFF0000 (http, RTP, ... L7 == APP_ID in many cases: ssh, ftp)
# APP_ID == ct_mark/0x0000FFFF (facebook, gmail, bittorrent, SQL, SNMP, CIFS, Exchange, TFTP, …)
# Drop ssh on non regular ports (L7 proto == 0xc6)
ovs-ofctl add-flow br0 "table=2,ct_mark=0x00c60000/0x7FFF0000,ip,tcp,tcp_dst=22,action=NORMAL"
ovs-ofctl add-flow br0 "table=2,ct_mark=0x00c60000/0x7FFF0000,ip,tcp,tcp_src=22,action=NORMAL"
ovs-ofctl add-flow br0 "table=2,priority=1,ct_mark=0x00c60000/0x7FFF0000,ip,action=drop"
# Rate limit bittorrent (L7 proto == 0xf)
ovs-vsctl -- set Port $CLIENTPORT_NAME qos=@newqos -- \
--id=@newqos create QoS type=linux-htb other-config:max-rate=1000000000 queues=0=@q0,1=@q1 -- \
--id=@q0 create Queue other-config:min-rate=1000000000 other-config:max-rate=1000000000 -- \
--id=@q1 create Queue other-config:min-rate=4000000 other-config:max-rate=4000000
ovs-ofctl add-flow br0 "table=2,priority=2,ct_mark=0x000f0000/0x7fff0000,ip,action=set_queue:1,NORMAL"
# Let all other traffic pass
ovs-ofctl add-flow br0 "table=2,priority=0,action=NORMAL"

## Slide 21: Demo part1: start-up
ICMPv6 (DAD)

## Slide 22: Demo part1: ssh on port 22, pass
Classification in progress (ct_mark == 0)
ARP

## Slide 23: Demo part1: ssh on port 5022, drop
no way to connect…

## Slide 24: Demo part1: large wget, full speed
Immediate!

## Slide 25: Demo part1: same file, but downloaded via bittorrent
Slow!
Torrent download via scp (ssh)
Tracker: L7=http, app=bittorrent
BITTORRENT file-transfer

## Slide 26: Annexes
L7 classification insights
Demo part 1: configuration details & step by step screenshots
Demo part 2: screenshots

## Slide 27: Demo2: initial chains

## Slide 28: Demo2: initial ACL & ACEs

## Slide 29: Demo2: ssh on port 5022, Encrypted chain

## Slide 30: Demo2: HTTP, Default chain

## Slide 31: Demo2: add FILE_TRANSFER chain

## Slide 32: Demo2: create new RSP

## Slide 33: Demo2: update ACEs

## Slide 34: Demo2: Final ACL/ACEs

## Slide 35: Demo2: go through the new FILE_TRANSFER chain