## Slide 1: All or Nothing The Challenge of Hardware Offload
__________________________________
December 5, 2018
Dan Daly

## Slide 2: Feature Log
Network
VM,
Container
or Server
Interface
Security
Virtualization
Visibility
Redundancy

## Slide 3: HW Offload (First Attempt)
Network
VM,
Container
or Server
Interface
Security
Virtualization
Visibility
Redundancy
HW Interface
Virtualization
Redundancy
Redundancy
How to Fix This?
Rule #1: No Specials
Rule #2: Offload is All or Nothing
Interface
Security
Virtualization
Visibility
Redundancy
Notes: Rule #1: Some software is more difficult to change than hardware, so adding ‘HW Specials’ isn’t acceptable
Rule #2: Having hand-offs between HW and SW takes away from the value, adds complexity, and special cases. This is challenging as the feature set needed is moving pretty rapidly, usually much faster than a regular hardware cadence

## Slide 4: Following the Rules
Adopt Existing VM Interfaces (containers & bare metal too)
Adopt Existing OVS Interfaces (use it for connection tracking too)
An Exact Match of the Data Plane (hw stats, mirroring, state tracking)
Requires Re-Programmable, Adaptable Hardware
Virtualized Server
VM
virtio
vSwitch
Slow Path
Smart NIC
vHost + OVS
Fast Path
Con-
tainer
virtio
Bare Metal Server
Smart NIC
vSwitch
Slow Path
vHost + OVS
Fast Path
virtio

## Slide 5
Server
Virtio Host Interface
VM
virtio-net
Open vSwitch
NIC
Server
VM
virtio-net
Open
vSwitch
SmartNIC
Hardware
Fast Path
Redundancy
Redundancy
Benefits:
No change in VM
Increased throughput & frame rate
Reduced latency
Free up cores in server
Hardware isolation between VMs
Seamless VM Migration

## Slide 6
Server
Bare Metal Hosting
NIC Driver
Benefits:
Hardware Agnostic Driver Interface
Brings OVS feature set to bare metal
Avoids network bottlenecks
Disaggregation
of Network Functions
Simple ToR Switch
SmartNIC
Server
virtio-net
Hardware
Fast Path
vSwitch
Slow Path
ToR Switch
(Tunnel endpoint)
Standard NIC
vRouter Appliance for multiple server racks

## Slide 7: OVS Programming Interface
Two Options:
tc-flower
Existing megaflow interface
Virtualized Server
VM
virtio
vSwitch
Slow Path
Smart NIC
vHost + OVS
Fast Path
Con-
tainer
virtio
Bare Metal Server
Smart NIC
vSwitch
Slow Path
vHost + OVS
Fast Path
virtio
https://www.usenix.org/system/files/conference/nsdi15/nsdi15-paper-pfaff.pdf

## Slide 8: Megaflow Based Offload – Architecture
OVS slowpath/vswitchd
vxlan
megaflows cache
Kernel
Userspace
HW
Kernel
sw conntrack
Kernel pipeline
Kernel pipeline
Hardware flow cache
hw conntrack
OF Table
OF Table
OF Table
hw device
DPIF-NETLINK
1st - OF Table Lookup
3rd - Hardware Lookup
2nd - Megaflow Lookup

## Slide 9: Megaflow Based Offload - Advantages
1. Faster than offloading through tc-flower
  TC isn’t required to keep copies of flows
  Avoid context switch for tunnels and connection tracking
  Fewer CPU cycles in slowpath
2. Simpler to maintain and deploy
  No netdev-linux HW offload path in dpif-netlink
  Less kernel version dependence
  Less kernel modules interactions (vxlan, netfilter)
3. Leverage Adaptable Hardware
  Let hardware handle connection tracking
  Application Aware Steering
Virtualized Server
VM
virtio
vSwitch
Slow Path
Smart NIC
vHost + OVS
Fast Path
Con-
tainer
virtio

## Slide 10: An Exact Match of the Data Plane
Some Software- Extremely hard to change
Anything in a customer VM
Kernel upgrades are no fun
At the same time, vSwitch requirements are moving extremely fast
Tunneling, connection tracking, telemetry, mirroring, failover
Intel Approach
Build Programmable, Adaptable Hardware (see next session)