## Slide 1: OvS Port Mirroring Offload
Tim Miskell, Liang-min Wang, Emma Finn, Edwin Verplanke (Intel)
Munish Mehan (AT&T)
December 7-11, 2020 | Virtual Event
Notes: Hello my name is Tim Miskell, a Solution Architect as part of the Network & Edge Platform Division at Intel.
Joining me today will be Larry Wang also from NEPD at Intel along with Munish Mehan from AT&T.
Together we will be discussing Intel and AT&T’s joint initiative regarding performance improvements to OvS port mirroring through hardware offload.

## Slide 2: Agenda
OvS Port Mirroring Use Case & Challenges
OvS-DPDK Port Mirroring via NIC HW Offload
OvS-DPDK Port Mirroring RFC Benchmarking
OvS-DPDK Port Mirroring RFC Demo
Call for Action
Notes: The topics for this presentation will include:
- Some background context on the use case and challenges related to TaaS performance in an OvS environment.
Our proposal for performance improvements to port mirroring via NIC HW offloading.
The benchmark data that we have collected showcasing the potential performance gains as part of our RFC.
A live demo of the actual RFC so that others may also experiment within their environment
And lastly a call for action in the hopes of providing grounds for additional discussion amongst the community for potential future directions for port mirroring.

## Slide 3: OvS Port Mirroring Use Case & Challenges
Probes will monitor 100% of the Mobility control plane traffic.
Probes will also monitor the Mobility user plane traffic.
Both Control Plane and User Plane components are virtualized and run on KVM with SRIOV and OVS-DPDK data path.
Packet acquisition will be orchestrated via the Openstack Tap as a Service (TaaS) feature.
Mirroring is costly in virtualized environment impacts performance and capacity, if it cannot be offloaded.
OVS-DPDK mirroring is done in software and has 70%+ impact.
OVS-DPDK East-West traffic – between VNFs on same host cannot be offloaded

## Slide 4: OvS Port Mirroring Use Case
High Level Diagram of setup
On Prem Telco
Cloud
KVM Computes
vGW
vGW
Aux Service VNF
vProbe
vProbe
vProbe
OVS-DPDK
NIC
NIC
VF
VF
VF
VF
SRIOV Packet Mirroring
OVS DPDK Packet Mirroring
SRIOV Packet Mirroring

## Slide 5: OvS-DPDK Port Mirroring Implementation Deep-Dive
Virtio Port Mirroring Packet Flow
Source VM to OvS
  Vhost Dequeue with Copy
OvS to Destination VM
  Vhost Enqueue with Copy:
    Vhost fetch available
    Vhost Copy
    Vhost Enqueue
OvS to vProbe VM (default)
  Vhost Enqueue with Copy
    Same copy sequence
OvS to vProbe VM (RFC)
  Leverage SR-IOV
  Transport via mirror channel
  In-place data transfer from mirror channel to vProbe
OVS-DPDK
NIC
vhost
vhost
vhost
VM1 （SRC）
VM2（DST）
VM3
QEMU
QEMU
QEMU
virtio-pci
virtio-pci
virtio-pci [1]
vProbe
(DPDK)
DeQ w/ Copy
EnQ w/ Copy
Copy
Fetch
EnQ
EnQ/Oflloading
Data Flow
Problem: Virtio port mirroring results in up to 70% performance impact
Root cause: Virtio mirroring requires 2x additional copies
Solution: NIC offloading

## Slide 6: OvS-DPDK Port Mirroring via NIC HW Offload
Host Network Interface (HNI):
  Manages device mirror configuration
Service Network Interface
  Vhostuser or Vhost PMD
Mirror Channel Network Interface
  Either:
    HNI
    SR-IOV interface managed by HNI
Monitor Service Network Interface
  SR-IOV instance managed by HNI

## Slide 7: OvS-DPDK Port Mirroring HWOL System Design
Notes: Make double arrow
Add in “new mirror configuration”

## Slide 8: OvS-DPDK Port Mirroring Developments
Extend ovs-vsctl mirror schema
  mirror-offload
  flow-dst-addr
  bond-port-other
  output-port-name
  output-src-vlan
  output-dst-vlan
Dependencies
  Unified mirror offloading configuration

## Slide 9: OvS Parameter Changes for Port Mirroring HWOL
Vhostuserclient/server port creation & configuration
  ovs-vsctl --no-wait add-port br-int vnic1 tag=1 -- set Interface vnic1
  type=dpdkvhostuserclient options:vhost-server-path=/tmp/vnic1
  options:n_rxq=1 other_config:pmd-rxq-affinity=… mtu_request=$mtu
Vhost PMD (vdev) port creation & configuration
  ovs-vsctl --no-wait add-port br-int vnic1 -- set Interface vnic1
  type=dpdk options:dpdkdevargs=net_vhost1,iface=/tmp/vnic1,queues=1,client=1
  options:n_rxq=1 other_config:pmd-rxq-affinity=… mtu_request=$mtu
DPDK port (mirror channel) creation and configuration
  ovs-vsctl --no-wait add-port br-int vnic1 -- set Interface vnic1
  type=dpdk options:dpdk-devargs=… options:tx_vlan_insert=true
  options:n_rxq=1 other_config:pmd-rxq-affinity=… mtu_request=$mtu

## Slide 10: Port Mirroring HWOL Configuration Examples
Egress Traffic Mirroring
ovs-vsctl -- set bridge br-int mirror=@m1 -- --id=@vnic1 get port vnic1 \
-- --id=@m1 create mirror name=… mirror-offload=1 select-src-port=@vnic1
output-port-name=dpdkbond0 output-src-vlan=4095
Ingress Traffic Mirroring
ovs-vsctl -- set bridge br-int mirror=@m2 -- --id=@vnic1 get port vnic1
-- --id=@m2 create mirror name=… mirror-offload=1 select-dst-port=@vnic1
output-port-name=dpdkbond0 output-dst-vlan=4095
Per-flow Traffic Mirroring
ovs-vsctl -- set bridge br-int mirror=@m3 -- --id=@vnic1 get port vnic1
-- --id=@m3 create mirror name=… mirror-offload=1 select-src-port=@vnic1
flow-dst-mac=“52\:54\:00\:00\:00\:01” output-port-name=dpdkbond0 output-vlan=4095

## Slide 11: OvS Port Mirroring RFC Benchmarking
Default Mirroring Test Setup
  Traffic Generator: pktgen
  DUT VNF: l2fwd
  vProbe TaaS: testpmd
    To verify throughput
  Intel® Ethernet Controller 700 Series XXV710
  Default mirroring enabled
    vnic1 (DUT VM)  vnic3 (vProbe)
Notes: Hello again my name is Tim Miskell and in the next two slides we’ll be presenting an overview of the topology used as part of our performance benchmarking.
As part of the default mirroring test setup, we make use of a traffic generator hosted on a separate server, in this case pktgen.
We run the DPDK l2fwd application as our VNF along with testpmd for our TaaS. Note that we primarily run testpmd on our vProbe VM in order to verify that the throughput matches the ingress/egress throughput as seen by the DUT VM.
We run the performance benchmarks on Intel® Ethernet Controller 700 series 25 Gbps NICs and we enable mirroring using the default mechanisms provided by OvS to mirror packets from vnic1 attached to port 0 on the DUT VNF to vnic3 attached to port 0 on the vProbe VM.
Note that the yellow dotted lines illustrate the original traffic flow, while the orange dotted lines illustrate the mirrored traffic flow.
Also note that our configuration includes an active-backup bond between the VFs for a more realistic scenario, with VF0 serving as the active port, and VF1 serving as the backup port. This setup can certainly be simplified further by removing the bond.

## Slide 12: Port Mirroring
HW Offload Test Setup
  Traffic Generator: pktgen
  DUT VNF: l2fwd
  vProbe TaaS: testpmd
    To verify throughput
  Intel® Ethernet Controller 700 Series XXV710
  HWOL mirroring enabled
    vnic1 (DUT VM)  VF1 (br-phy)
    VLAN mirroring enabled from VF1 (br-phy)  VF3 (vProbe)
Notes: The following slide presents our test setup in the case where we benchmark enabling hardware offload as part of our RFC.
The setup is identical to the previous slide with the following notable exceptions:
We create 2 additional virtual functions, shown in orange, 1 for each VF part of the original active-backup bonding configuration. Both of these new VFs are attached to our vProbe VM.
We mirror packets from the vnic1 attached to port 0 on the DUT VNF to VF1, the standby port attached to our OvS bridge.
In addition to this, we also enable VLAN mirroring, through our hardware offload interface VFd, to mirror packets from VF1 from our OvS bridge to VF3 attached to the vProbe VM.

## Slide 13: Notices & Disclaimers
Performance varies by use, configuration and other factors. Learn more at www.Intel.com/PerformanceIndex​.
Performance results are based on testing as of dates shown in configurations and may not reflect all publicly available ​updates. See backup for configuration details. No product or component can be absolutely secure.
Your costs and results may vary.
Intel technologies may require enabled hardware, software or service activation.
© Intel Corporation. Intel, the Intel logo, and other Intel marks are trademarks of Intel Corporation or its subsidiaries. Other names and brands may be claimed as the property of others.

## Slide 14: Performance Data
Chart: DPDK 20.08 l2fwd, 2x Virtio, 1C1T / Virtio, MRR, RX Throughput, Ingress Mirroring OvS Master, DPDK 19.11.5, i40e 2.12.6.3, 1x RX Port Mirror RXQ = TXQ = 1
| 64 | 128 | 256 | 512 | 1024
Mirroring Disabled | 6.3591 | 5.9853 | 5.444 | 4.0621 | 2.9873
Default Ingress Mirroring Enabled | 1.7825 | 1.6745 | 1.4945 | 1.1526 | 0.91767
Ingress Mirroring HWOL Enabled | 4.7864 | 4.5531 | 4.1719 | 3.2874 | 2.1812
Ingress and Egress Mirroring1
+168.5%
Chart: DPDK 20.08 l2fwd, 2x Virtio, 1C1T / Virtio MRR, TX Throughput, Egress Mirroring OvS Master, DPDK 19.11.5, i40e 2.12.6.3, 1x RX Port Mirror RXQ = TXQ = 1
| 64 | 128 | 256 | 512 | 1024
Mirroring Disabled | 5.5757 | 5.2954 | 4.5713 | 3.0939 | 2.134
Default Engress Mirroring Enabled | 1.703 | 1.5879 | 1.418 | 1.0556 | 0.8751
Engress Mirroring HWOL Enabled | 4.3232 | 4.1552 | 3.8166 | 3.0582 | 2.1392
+153.9%
1 - See SLIDE 19 for workloads and configurations. Results may vary​. Performance varies by use, configuration and other factors. Learn more at www.Intel.com/PerformanceIndex. Testing conducted on OvS-DPDK software comparing Intel® Xeon® Gold 6139 processor, Intel® Ethernet Controller XXV710 with and without mirror hardware offload. Platform: S2600WFQ, BIOS: SE5C620.86B.02.01.0012.070720200218, Turbo: Disabled. Testing done by Intel.
Notes: Moving now to the performance data captured as part of this benchmark, we ran four different test case scenarios specifically:
Ingress mirroring
Egress mirroring
Per-flow ingress mirroring
And per-flow egress mirroring.
The following slide presents the OvS master DPDK 19.11 MRR l2fwd single queue RX and TX throughput data, respectively for the ingress and egress mirroring test cases.
In this case the light gray bar on the left represents the baseline where mirroring is disabled, the dark gray bar in the middle represents the case where mirroring is enabled using the default OvS mechanisms, and the gray bar on the right represents the case where mirroring is enabled using NIC hardware offloading.
As previously mentioned, the performance degradation to the DUT VNF when default mirroring is enabled reaches approximately 70%, particularly in the case of 64 B packets.
We observe a performance improvement up to 168% when mirroring via NIC HW offload is enabled.

## Slide 15: Performance Data
Chart: DPDK 20.08 l2fwd, 2x Virtio, 1C1T / Virtio MRR, RX Throughput, Per-flow Ingress Mirroring OvS Master, DPDK 19.11.5, i40e 2.12.6.3, 1x RX Port Mirror RXQ = TXQ = 1
| 64 | 128 | 256 | 512 | 1024
Mirroring Disabled | 6.3591 | 5.9853 | 5.444 | 4.0621 | 2.9873
Default Per-flow Ingress Mirroring Enabled | 1.7998 | 1.6808 | 1.5247 | 1.141 | 0.9306
Per-flow Ingress Mirroring HWOL Enabled | 4.7362 | 4.5094 | 4.1592 | 3.2543 | 2.1139
Per-flow Ingress and Egress Mirroring1
+163.1%
1 - See SLIDE 19 for workloads and configurations. Results may vary​. Performance varies by use, configuration and other factors. Learn more at www.Intel.com/PerformanceIndex. Testing conducted on OvS-DPDK software comparing Intel® Xeon® Gold 6139 processor, Intel® Ethernet Controller XXV710 with and without mirror hardware offload. Platform: S2600WFQ, BIOS: SE5C620.86B.02.01.0012.070720200218, Turbo: Disabled. Testing done by Intel.
Chart: DPDK 20.08 l2fwd, 2x Virtio, 1C1T / Virtio MRR, TX Throughput, Egress Mirroring OvS Master, DPDK 19.11.5, i40e 2.12.6.3, 1x RX Port Mirror RXQ = TXQ = 1
| 64 | 128 | 256 | 512 | 1024
Mirroring Disabled | 5.5757 | 5.2954 | 4.5713 | 3.0939 | 2.134
Default Engress Mirroring Enabled | 1.703 | 1.5879 | 1.418 | 1.0556 | 0.8751
Engress Mirroring HWOL Enabled | 4.3232 | 4.1552 | 3.8166 | 3.0582 | 2.1392
+153.9%
Notes: The following slide presents the MRR RX and TX throughput respectively for per-flow ingress and per-flow egress mirroring, specifically with 100% matching flows sent to the l2fwd DUT VNF in the interest of a more apples-to-apples comparison with the data collected for port ingress and egress mirroring.
The test results shown above are almost identical to the ones shown in the previous slide, particularly given that the destination MAC address for each packet sent by our traffic generator matches the DUT VNF.
As before we observe up to 70% performance degradation to the DUT VNF, which improves up to 163% when mirroring via NIC HW offload is enabled.

## Slide 16: OvS Port Mirroring RFC Demo
Baseline
Default Port Mirroring
Port Mirroring with HW Offload (RFC)
Notes: We’ve now reached the live portion of the presentation where we will demonstrate performance in three cases, namely:
Baseline RX throughput performance of the DUT VNF with mirroring disabled
RX throughput performance of the DUT VNF when ingress port mirroring is enabled using the default OvS mechanisms
RX throughput performance of the DUT VNF when ingress port mirroring is enabled via NIC HW offloading
Note that in all cases we send 64 B packets.

## Slide 17: Call for Action
OvS RFC:
  https://www.mail-archive.com/ovs-dev@openvswitch.org/msg45745.html
Unified Device Mirroring Configuration
  DPDK PF Driver
    Add mirroring option, from PF to SR-IOV device, on rte_flow or rte_eth API
  Kernel PF Driver
    Add mirroring option, from one SR-IOV to another SR-IOV device
  Leave configuration outside of OvS
    I.e., system administrator configures device mirroring
Replace VHOST data copy with DMA CPU offload

## Slide 18: Thank You!
For more information:
AT&T:
  Munish Mehan: mm6021@att.com
Intel:
  Liang-min Wang: liang-min.wang@intel.com
  Tim Miskell: timothy.miskell@intel.com
Notes: Thank you to everyone for your time, we will now conclude this presentation for OvS port mirroring and allow time for questions, thoughts and comments.
Please also feel free to reach out for more information about the work that was presented today.

## Slide 19: System Config
 | Config1 (Default Mirroring) | Config2 (RFC Mirroring)
Test by | Intel | Intel
Test date | 11/13/2020 | 11/13/2020
SUT Setup |  | 
Platform | S2600WFQ | S2600WFQ
# Nodes | 1 | 1
# Sockets | 2 | 2
CPU | Intel(R) Xeon(R) Gold 6139 CPU @ 2.30GHz | Intel(R) Xeon(R) Gold 6139 CPU @ 2.30GHz
Cores/socket, Threads/socket | 18/36 | 18/36
Microcode | 0x2006906 | 0x2006906
HT | On | On
Turbo | Off | Off
Power management | intel_pstate driver disabled | intel_pstate driver disabled
Sub Numa cluster | Disabled | Disabled
Prefetcher | MLC & DCU Enabled LLC Disabled | MLC & DCU Enabled LLC Disabled
BIOS version | SE5C620.86B.02.01.0012.070720200218 | SE5C620.86B.02.01.0012.070720200218
AEP FW version – E.g. 5336 | N/A | N/A
System DDR Mem Config: slots / cap / speed | 6slots / 32GB / 2666 MT/s | 6slots / 32GB / 2666 MT/s
System PMem Config: slots / cap /speed | N/A | N/A
Total Memory/Node (DDR, PMem) | 192 GB, 0 GB | 192 GB, 0 GB
Storage - boot | 1x INTEL SSDSCKKI25 256GB SATA OS Drive | 1x INTEL SSDSCKKI25 256GB SATA OS Drive
Storage - application drives | N/A | N/A
NIC | 2x Intel Corporation Ethernet Controller XXV710 for 25GbE SFP28 | 2x Intel Corporation Ethernet Controller XXV710 for 25GbE SFP28
PCH | Intel C628 | Intel C628
Other HW (Accelerator) | N/A | N/A
Client Setup |  | 
Platform | S2600WT2R | S2600WT2R
# Nodes | 1 | 1
# Sockets | 2 | 2
CPU | Intel(R) Xeon(R) CPU E5-2699 v4 @ 2.20GHz | Intel(R) Xeon(R) CPU E5-2699 v4 @ 2.20GHz
Microcode | 0xb000038 | 0xb000038
HT | On | On
Turbo | On | On
System DDR Mem Config: slots / cap / speed | 2slots / 32GB / 2666 MT/s | 2slots / 32GB / 2666 MT/s
Storage | 1x INTEL SSDSC2BA80 800 GB SATA OS Drive | 1x INTEL SSDSC2BA80 800 GB SATA OS Drive
NIC | 2x Intel Corporation Ethernet Controller XXV710 for 25GbE SFP28 | 2x Intel Corporation Ethernet Controller XXV710 for 25GbE SFP28