## Slide 1: vswitch.p4: Why OVS Needs P4
Open vSwitch and OVN 2020 Fall Conference
Presenter: Dan Daly
Intel P4-OVS Team: Dan Daly, Anjali Singhai, James Choi, P. Venkata Suresh Kumar, Namrata Limaye, Debashis Chatterjee

## Slide 2: Notices & Disclaimers
Performance varies by use, configuration and other factors. Learn more at www.Intel.com/PerformanceIndex.
Performance results are based on testing as of dates shown in configurations and may not reflect all publicly available updates. See backup for configuration details. No product or component can be absolutely secure.
Your costs and results may vary.
Intel technologies may require enabled hardware, software or service activation.
© Intel Corporation. Intel, the Intel logo, and other Intel marks are trademarks of Intel Corporation or its subsidiaries. Other names and brands may be claimed as the property of others.

## Slide 3: Why P4 in OVS? Information Encoding
Notes: - Why P4 in a host? Why P4 in OVS?
- Encoding More Information than OpenFlow
- - Explicit match types, actions and control flow
- - Enable dataplane optimizations
- - Better constrained random testing (define the combos you need, nothing you don’t, and test them)
- No More Priority Based If-Clauses
- - OpenFlow conditionals using priority (yuck)
- - Explicit control flow between matches and action (yay)
- Whole Datapath Approach
- - Encode the underlying network structures
- - - Ports, Teams, Routes, Tunnels
- - Encode the translation tables
- - - iptables NAT, VLAN tagging, netdev tagging
- - Preserve the existing control planes
- Enable a full dataplane offload
- Yes, Connection Tracking Too
- - I can keep this brief if someone else is going deep on this
- Kernel Control Planes, SDN vSwitch, Hardware Datapath
- - Outline the Kernel - SAI connection used in SONiC
- - Netlink socket listeners
- Summary
- - P4 encodes more information than OpenFlow
- - - Better for optimization, easier to validate
- - New! P4 can now encode the whole datapath
- - - Explicit Connection Tracking
- - - IPSec Tunnels
- - One Datapath definition of everything that processes packets
- - - Provides a complete ‘spec’ that can be targeted to different data planes, including hardware
- - - Provides customization path where it is clear what goes where in what order

## Slide 4: What Information to Encode?
Specific instead of generic →
  Better optimized pipeline implementations
  Auto-generated testing of what matters
Kernel operations in the datapath →
  Enables an optimized kernel path w/out bypassing
Program more operations →
  Cambrian explosion of networking applications
Network as a programmable platform →
  Programs to measure, validate, & re-program the network
Notes: - Why P4 in a host? Why P4 in OVS?
- Encoding More Information than OpenFlow
- - Explicit match types, actions and control flow
- - Enable dataplane optimizations
- - Better constrained random testing (define the combos you need, nothing you don’t, and test them)
- No More Priority Based If-Clauses
- - OpenFlow conditionals using priority (yuck)
- - Explicit control flow between matches and action (yay)
- Whole Datapath Approach
- - Encode the underlying network structures
- - - Ports, Teams, Routes, Tunnels
- - Encode the translation tables
- - - iptables NAT, VLAN tagging, netdev tagging
- - Preserve the existing control planes
- Enable a full dataplane offload
- Yes, Connection Tracking Too
- - I can keep this brief if someone else is going deep on this
- Kernel Control Planes, SDN vSwitch, Hardware Datapath
- - Outline the Kernel - SAI connection used in SONiC
- - Netlink socket listeners
- Summary
- - P4 encodes more information than OpenFlow
- - - Better for optimization, easier to validate
- - New! P4 can now encode the whole datapath
- - - Explicit Connection Tracking
- - - IPSec Tunnels
- - One Datapath definition of everything that processes packets
- - - Provides a complete ‘spec’ that can be targeted to different data planes, including hardware
- - - Provides customization path where it is clear what goes where in what orde

## Slide 5: 1. Be Specific
P4 Encodes:
Control Flow: Order of Operations
Match Types: Not Everything Has to Be Ternary
Specific Actions: Specify the actions needed
Enables a Compiler to Target Dataplanes ↓
Platform
Switch
SmartNIC
Software
FPGA
P4 Studio
P4 Compiler Front-end
P4 Visualization
C Model
Pipeline
SDK
Switch Back-end
C Model
Pipeline
SDK
NIC Back-end
Pipeline
SDK
Software Back-end
table routing {
key = { ipv4.dstAddr : lpm; }
actions = { drop; route; }
size : 2048; }
control ingress() {
apply {
routing.apply(); }
}
P4 Program
Hardware
SDK
FPGA Back-end
More info: Converting OpenFlow to P4
C Model

## Slide 6: 2. Kernel Powered
New! P4 can encode the supporting kernel operations
  Tunnels, Routes, Conntrack, IPSec Tunnels, iptables
PNA – Portable NIC Architecture
  Portable across different targets
  New constructs for Connection Tracking, IPSec, Message Handling
Kernel configuration relayed to P4 dataplane via SAI
  See SONiC synchronization msgs (https://github.com/Azure/SONiC/)
Whole Datapath Approach
More info: Container Networking w/ OVS
Notes: - Why P4 in a host? Why P4 in OVS?
- Encoding More Information than OpenFlow
- - Explicit match types, actions and control flow
- - Enable dataplane optimizations
- - Better constrained random testing (define the combos you need, nothing you don’t, and test them)
- No More Priority Based If-Clauses
- - OpenFlow conditionals using priority (yuck)
- - Explicit control flow between matches and action (yay)
- Whole Datapath Approach
- - Encode the underlying network structures
- - - Ports, Teams, Routes, Tunnels
- - Encode the translation tables
- - - iptables NAT, VLAN tagging, netdev tagging
- - Preserve the existing control planes
- Enable a full dataplane offload
- Yes, Connection Tracking Too
- - I can keep this brief if someone else is going deep on this
- Kernel Control Planes, SDN vSwitch, Hardware Datapath
- - Outline the Kernel - SAI connection used in SONiC
- - Netlink socket listeners
- Summary
- - P4 encodes more information than OpenFlow
- - - Better for optimization, easier to validate
- - New! P4 can now encode the whole datapath
- - - Explicit Connection Tracking
- - - IPSec Tunnels
- - One Datapath definition of everything that processes packets
- - - Provides a complete ‘spec’ that can be targeted to different data planes, including hardware
- - - Provides customization path where it is clear what goes where in what orde

## Slide 7: P4 Referencing Kernel Objects via SAI
P4 match/action w/ Kernel (SAI) objects
SAI+P4 Table Entries Populated via P4Runtime:
Match on { Header, Virtual Port Metadata } → Set VNI / Geneve.{source,dest} Metadata, Encap( SAI Tunnel Handle, VNI, Geneve.{source,dest} )
Remaining pipeline logic is populated through the kernel (via SAI):
Match on { VRF : exact, Metadata Dest IP : LPM } → Route
Action Selector for NextHop, Interface
vSwitch
Pipeline
Kernel
(via SAI)
(Tunnel,
Route,
Forward)
Ports
VMs
Transmit Flow Example

## Slide 8: 3. Program More = Explosion of Accelerated Workloads
Networking
P4
Compiler
Programmable
Data Planes
Cloud Switching
Enterprise/Telco/SP Switching
E2E Telemetry & Analytics (INT)
Adv Congestion Control
Firewall & DDoS
Accelerated VNFs
Network Packet Broker
DNS Cache
Pattern Matching & Stream Processing
Key Value Caching & Replication
Extremely-Accurate Time Synchronization
Consensus Acceleration
Storage Interconnect
More…
Microservices Acceleration
Machine Learning Fabrics
Programmable Data Planes
Notes: #1: If you’re a just fixed-function switch, there are only two things you can do: telco and cloud switching (in blue boxes). But with P4 programmability, it opens pandoras box on what types of applications you can create and implement.
1a) The different colors illustrated above are grouping the different types of new apps together.
#2: What can you do with P4 beyond Tofino? Combining Tofino with other programmable devices like NIC, FPGA, CPU, you can create richer applications to further expand the market applicability.
*On the next slide, we will focus on end-to-end telemetry and analytics

## Slide 9: 4. Network as a Programmable Platform
NIC
NIC
Control Plane
Control App
Control App
Control App
Control App
Fine-grained Per-packet Measurement (e.g. INT)
Generation & Verification
Control state/code
Contract
Dataplane state/code
Switch OS
switch
switch
switch
NIC
NIC
-OVS
-OVS
Runtime Contract
Switch OS
Switch OS
DPDK
XDP
vswitch.p4

## Slide 10: vSwitch Programmable Platform
Current: OpenFlow + OVSDB
OpenFlow ordered tables w/ priority-based ‘jumps’
Escapes to kernel functions Conntrack, tunnels, iptables
Proposal: P4 + OVSDB
P4 control flow w/ typed matches & actions Converting OpenFlow to P4
Explicit dataplane functions Conntrack, tunnels, iptables Container Networking w/ OVS
Use P4 to Encode Network Intent

## Slide 11: vswitch.p4
Reflected Kernel Datapath
  Ports, Teams, Routes, Tunnels, NAT, load balancing, conntrack
OpenStack Neutron Feature Set
  vL2, vL3, Security Groups, vLB
OVN & Antrea examples
Jumpstart Your.p4
SDN Controller / Agent
L2
L2
L3
L2
L2
LB
L2
L2
L2
ACLs
Security Groups
+
P4
Runtime
P4 RT
Config
RPC
ovsdb
Tunnel
ILA
L3
L2
BGP
ECMP
FDB
team
Ports
Re-usable
tests

## Slide 12: vswitch.p4
vswitch.p4 → Your.p4 Customize, Optimize
Compile for Target(s) Capabilities, Scale, Fit
Dataplane Load Population w/ P4 APIs
(Optional) Dataplane Update
Open Source Project
P4.org
vswitch.p4
PSA Specification
PNA Specification
P4_16 Specification
How it comes together

## Slide 13: Why P4 in OVS?
P4 encodes more information than OpenFlow
  Better for optimization, validation & re-programming
  New! P4 can now encode the Whole Datapath
P4 in OVS : More programmable, flexible & multi-target
vswitch.p4 encodes common functionality to get started
What Will You Do With This Added Programmability?

## Slide 14: Contacts
Code will be uploaded on Github. Please email for more info…​
Contacts: Debashis Chatterjee (Debashis.Chatterjee@intel.com)​
Dan Daly (dan.daly@intel.com)​
Intel P4-OVS Team: Dan Daly, Anjali Singhai, James Choi, P. Venkata Suresh Kumar, Namrata Limaye, Debashis Chatterjee