## Slide 1: Better exception path for OVS-DPDK
Thilak Raj Surendra Babu Nutanix

## Slide 2: Problem statement
A packet over bro interface in OVS-DPDK endures an additional HOP in comparison with OVS-KERNEL.
VIRTIO-user as an exception path seems to give relatively better performance but consumes another thread.
VIRTIO-user as dpdk-dev args in the current form doesn’t make use of any GRO/TSO offloads.

## Slide 3: Challenges
VIRTIO-user while improves performance take an additional thread.
OVS-DPDK doesn’t handle multi-segment mbufs.
Tap
VIRTIO USER
Eth
NIC
Smaller Packets
OVS- DPDK
Vhost-net thread

## Slide 4: Solution
User mergeable buffers on the VIRTIO interface
RX
  Packets in the vring are chained mbuf representing a coalesced TCP packet.
  Construct a new mbuf by creating a large external mbuf.
  Set the meta data for the new mbuf accordingly.
  Transmit the packet.
TX
  Use rte_gro to coalesce the packets before sending them towards the VIRTIO user interface.
  Place the chained mbuf on the VIRT queue.
EXT mbuf
EXT mbuf
RX-VIRTQ
Copy chain into a external mbuf
Let ovs-dpdk handle a single mbuf
rte_gro
RX-Path
TX-Path
TX-VIRTQ
Gro processing emits a coalesced packet which is a chain
Packets belonging to various flows in a burst

## Slide 5: Results
Modified |  | 
Attribute | IPERF | IPERF -R
Vhost-net CPU Usage | 60% | 40%
BW | 9.34 | 9.1G
PMD CPU usage | 10%/90% | 3%/4%
Master |  | 
Attribute | IPERF | IPER -R
Vhost-net CPU Usage | 100% | 100%
BW | 6.5G | 8.4G
PMD CPU usage | 12%/66% | 2%/65%

## Slide 6: Thank you!