## Slide 1: Pluggable DPIF - Unlocking accelerated OVS full potential
RRoi Dayan, Roni Bar Yanai, Eli Britstein, Nov 2024
Notes: Slide#2: HW Acceleration is a must
Slide#3: How does HW acceleration works (slow path, rules offloading, etc.)

## Slide 2: HW Acceleration is a must
Evolving Cloud Workloads: Cloud applications demand extremely high bandwidth and low latency to meet modern performance requirements.
Performance Challenges:
Maintaining scalability under high-performance demands.
Handling processing speeds at hundreds of gigabits per second.
Open vSwitch (OVS) must leverage hardware acceleration to:
  Remain competitive in high-performance environments.
  Reduce CPU load.
  Low and constant latency
  High CPS
VM
QP
AI App
OVS
p0
p1
RoCE
HW
p0
p1
None accelerated
Accelerated

## Slide 3: OVS acceleration Journey
DPIF-NETlink (OVS-Kernel)
DPIF-NETDEV (OVS-DPDK)
OVS-P4
OVS-DOCA
OVS-DPDK
Open Flow
CLI
OVS
Future extensions
DPIF Netdev (DPDK)
Netdev Offload DPDK
OVS-Kernel
DPIF Netlink (Kernel)
Netdev Offload tc
DPDK rte_flow
DOCA Flow
tc
…
…
…
Hardware
Community
Community+NVIDIA
NVIDIA
Legend:

## Slide 4: DPIF-NETlink
TC (Linux traffic controller) is the acceleration API
OVS relies on the kernel for part of the data path, using TAP devices like VXLAN
  Packets leaving OVS to the kernel and returned via a different device lose context
Kernel components like routing tables, FIB, and netfilter are scattered
  Complex Synchronization (e.g. driver & routing table)
A holistic view of the packet pipeline is not achievable, packet cannot carry information between pipeline stages
SW is heavy (compared to less generic use case) and dictates slow CPS (CT)
OVS Kernel acceleration is non-optimal
While achieving significantly better performance compared to software and improving further with new hardware, the results are still far from the max possible performance
BR-EXT
BR-INT
vxlan
vxlan
VF ip
kernel
VF
p0
rep

## Slide 5: DPIF-NETDEV
OVS executes an end to end pipeline, packets are handled in run-to-completion (does not leave context and return out-of-the-blue). Offering better context (some used by EMC and SMC – OVS caches)
HW acceleration relies on DPDK-based rte_flow API
  rte_flow is a low-level API, allows redundant methods to achieve the same pipeline
  Vendors have unique limitations on supported matches and actions
  This creates API conflicts, making the API too low-level for generic use case
  The offload API at the netdev level lacks context. It provides the acceleration layer with only a narrow view of the pipeline
  Customers often use OVS-DPDK and develop their own acceleration layer on top of DPDK rte_flow
OVS-DPDK

## Slide 6: OVS-P4
There were few attempts to introduce P4 to OVS
OVS Datapath Specialization using P4 - OVS Conference 2015
IPDK - OVS with P4 Walkthrough 2022
OVS 2022 Conference - Using OVS with P4 Coprocessor
OfP4, a P4 front end for Open vSwitch
Eventually P4 is not part of OVS
Probably because P4 its too different than other acceleration API
The following architecture which has p4-dpif was suggested
A third acceleration API

## Slide 7: HW acceleration challenges with current OVS Arch

## Slide 8: Partial execution of pipeline actions
OVS uses Connection Tracking (CT) as an action
CT action can be placed after some packet modification already happened
CT miss requires SW involvement, but SW is now broken
CT as an example
ct_state(-trk),recirc_id(0),in_port(6),packet_type(ns=0,
id=0),eth(src=fa:16:3e:1f:66:29,dst=fa:16:3e:53:10:28),eth_type(0x0800),ipv4(src=172.16.0.101/128.0.0.0,proto=1,frag=no), packets:8, bytes:784,used:0.909s,actions:set(eth(src=fa:16:3e:fd:98:0c,dst=fa:16:3e:53:10:28)),push_vlan(vid=2,pcp=0),ct(zone=2,label=1209),recirc(0x5eb2)
What if this is a new connection that is not in HW. Packet was already modified, OVS SW might miss
The software receives a partially processed packet and may not know how to handle it. It must resume actions from where they stopped, which is challenging, leading to malfunctions and inconsistencies

## Slide 9: dP_HASH
DP_HASH runs “Jenkins hash” function on 5-tuple and than jumps to one of X buckets, who have actions
HW might have a different hash function than Jenkins or other SW implementation hash, leading to consistency issues between HW accelerated pipes and SW pipes, and causing network failures and e.g. tcp disconnections
Having SW & HW using the same hash could solve this problem (SW to use HW capability)
HW hash might be different than SW or other vendors
SW hash
Action A
Action B
Action C
Hash X
HW hash
Hash y
First packet might have a different path
Netdev 0x14 NVIDIA suggested a path, but it didn’t get through
Having SW and HW sync on hash is a must!

## Slide 10: Meter
Some packets reach the software, which might share the same meter
If the meter state is in hardware, packets in SW must be synched with it
Different HW might have different approaches to solve this problem
  Current solution is sending packet back to HW for metering
  NVIDIA plans to allow software to update the mete
  (not supported with current hardware)
Using always HW State
SW
HW

## Slide 11: OVS conntrack
HW may have its own connection tracking (CT) implementation
SW shadow is often unnecessary and consumes many cycles
HW might prefer alternative hardware-based approaches (making SW logic meaningless)
Why go to SW path?
HW CT
SYN/FIN/RST go to SW with flow index
Other packets continue in HW

## Slide 12: Aging
Mega-Flow
OVS tracks idle time for each mega flow
If the rule is in hardware, software counters won't advance
HW counters support are different across hardware types (e.g. Rx, Tx, before and after)
Ideally - HW rules would be aged out automatically (autonomously) while OVS just sets the time
  This requires OVS to be deeply hardware-acceleration aware
HW is very different
NVIDIA offers efficient hardware aging.
OVS only needs to call the API for aged-out flows, with no need for additional software involvement

## Slide 13: No Context
OVS data path has its own optimizations, like squeezing into EMC or SMC cache, this is dpif specific data path optimization
HW acceleration is currently below and has no context info (flow went through 3 CT tables, HW can handle one flow for the complete E2E)
SMC/EMC caches

## Slide 14: Summary
Missing HW based solutions like CT
Split state between HW and SW
Miss path (state of the flow in the middle)
Performance – what HW can do in best against current implementation
Other issues: threading model, support for security pipelines, memory management, etc.
Conclusion: DPIF NetDev requires major re-architecture changes to support the existing basic functionalities with different HW
HW acceleration has many challenges

## Slide 15: HW Acceleration is a data path
Going to the next level of performance

## Slide 16: Customers selected architecture
Customers that have their own flavor of OVS are usually:
  Forking DPIF-NETDEV
  Having their own completely unique OVS offload API HW offload that is strongly integrated with slow path
  Staying close to user space updates but have their own unique HW acceleration strategy
  Their offload API are based on:
    DPDK rte_flow (legacy usage)
    DOCA FLOW (recent engagements)
Generates their own DPIF!

## Slide 17: Integrated HW acceleration in Data path (DPIF)
Problem with accelerating existing data path (dpif-netdev, or dpif-netlink), disregarding the problems stated earlier
  Different strategies must be applied when using HW acceleration, e.g. mega-flow aging might overwhelm the SW control pipe
  Packet that had a miss in middle of HW flow and waited in queue might reach a point where it is not valid (hit different set of “old” rules in HW and now there are “new” rules in SW)  SW must be HW accelerated aware
  Moving from HW to SW and back to HW can cause significant cost in packet’s out-of-order
  Synchronization of HW flows and SW flows might look very different among non-common HW capabilities, for example, sync vs async API, latency, keys sizes, carrying information HW to SW…etc.
SW path must be HW accelerated aware

## Slide 18: Integrated HW acceleration in Data path (DPIF)
SW has some SW data path optimizations such as EMC/SMC, rebalance queues…etc.
HW cannot benefit from that. HW can benefit by applying a different set of optimizations which suitable for HW, and for a specific API
  Using HW specific strategies
  Since slow path handles much less packets, more time can be spent on optimizations
  Sharing resources
  Squeezing data plane rules (knowing HW is fast enough to do quick update)
  Having packets completing pipeline in HW
  First packet that generate mega-flow, is sent back to HW to execute
HW Optimizations

## Slide 19: Integrated HW acceleration in Data path (DPIF)
Slow Path and HW acceleration should be mixed
In some cases, packet should be sent to complete the pipeline in HW.
For example, when all a mega-flows are in place and only CT entry is missing for a new flow, it is much better to just send the packet back to HW with next recirc-id, and meta-data to continue the pipeline.
This is true also for the start point, if packet is missed on CT it should just go directly to CT code.
It might be that CT code is running on dedicate HW code.
Separating CT by itself is not good enough, but if separated is means this is vendor CT at least. The CT and mega flows share meta data that also must be defined, and CT sends packet back to HW.
In addition, this is just one possible model when using HW acceleration, different vendors might have different requirements.
CT
NIC
Logic
Mega flows
OVS
HW

## Slide 20: Conclusions
Offloading the existing data path cannot achieve optimal hardware performance. Like OVS-DPDK benefits from software optimizations, hardware acceleration requires unique, hardware-focused strategies
Hardware acceleration must be tightly integrated into the software data path. This integration depends on the hardware (e.g., P4 vs. DOCA Flow) and can differ significantly (Best solution must have an HW specific arch)
Having such integrated API that can hold different technologies will have a huge impact on dpif-netdev and community effort and might affect SW only performance
DPIF was already designed for holding different data paths (common API) and HW acceleration is just one of them
Loadable DPIF reduces community effort by being handled by their vendors, while keeping full compatability with OVS functionalities on the upper layer
Enables a formal and healthy adoption of what Is already happening anyway by customers
OVS can be continuously adopted and used in modern cloud tight requirements, with increased innovation
DPIF must be pluggable and HW specific for best datapath impact